## Slide 1: Vehicle Dynamics and Simulation
Dr B Mason
Drivetrain Dynamics

## Slide 2: Lecture overview

## Slide 3: The Drivetrain System

## Slide 4: The Drivetrain System

## Slide 5: The Drivetrain System
The drivetrain can be represented as a number of springs and masses
Each mass is isolated as a point-mass
These types of models are known as lumped parameter models
Control of vibration is achieved by;
  Reducing excitation
  Changing stiffness and damping (resonance frequencies)

## Slide 6: The simplest useful model
shuffle
rattle
Torsion
damper
Drive-
train
Engine inertia
Transmission
Vehicle inertia
Three main modes;
  Shuffle (4-12 Hz)
  Rattle (40 – 80 Hz)
  Rigid body rotation
And others;
  Boom (interior compartment)
  Judder (low frequency on clutch engagement)
  Clonk (lash in driveline)

## Slide 7: More advanced models
Three, four, six, …, twenty mass models
  Complexity driven by requirements
Can add masses to suit
Other components in the drivetrain are important
  Clutch
  Differential
  Actuators and related controls

## Slide 8: Standardised components
Spring-damper
Mass

## Slide 9: Response to step input